## Slide 1
Smart Motor Control in EVs using VFD
Variable Frequency Drives for Electric Vehicle Performance
Comprehensive Technical Analysis
BY-Anand V. Chavan
RA2512053010013

## Slide 2
Smart Motor Control in EVs using Variable Frequency Drives (VFD)
Introduction to VFD
What is a VFD?
A Variable Frequency Drive converts fixed-freq AC/DC power
into variable-frequency AC to control motor speed & torque.
Key Benefits:
· Optimal motor efficiency across speed range
· Precise torque control for accel. & braking
· Extended driving range via energy optimization
· Superior performance in all driving conditions
VFD Architecture & Specs
Signal Flow:
AC/DC Source → Rectifier → DC Link → Inverter → Motor
Controller (Microprocessor) manages Frequency & Voltage
Key Specifications:
Input: Battery 300–400 V DC
Output: Variable AC 0–120 Hz
Power: 100–300+ kW (vehicle class)
Control: μs-level precision for optimal response
Main Components
1. Rectifier
Converts AC to DC via diode/thyristor bridges
2. DC Link
Smooths voltage with capacitors; stabilizes bus voltage
3. Inverter
DC → variable-freq AC using IGBTs / MOSFETs
4. Controller
Executes control algorithms; manages switching sequences
Operating Principle
Speed Formula:
N = (120 × Frequency) / No. of Poles
Frequency Stages:
0 Hz – Motor standstill / zero speed
30 Hz – Low speed, maximum torque
60 Hz – Mid-range / highway cruising
120+ Hz – High-speed / performance mode
Motor Control Strategies
Vector Control (FOC)
Independent speed & torque control; excellent dynamic
response; most widely used in EVs.
Direct Torque Control (DTC)
Direct torque regulation; fast response; minimal delays;
superior for acceleration.
Model Predictive Control (MPC)
Predicts future behavior; optimizes efficiency; adapts
to variable conditions.
Vector Control (FOC) Flow
1. Read Motor Params (Speed, Current, Voltage)
2. Transform to dq Coordinates (Decoupling)
3. Calculate Flux & Torque Components
4. Apply PI Controllers for Speed & Current
5. Generate PWM Signals to Inverter
6. Output Optimized Motor Voltage & Frequency
DTC vs FOC Comparison:
Response: DTC Fastest · FOC Moderate
Efficiency: FOC Excellent · DTC Very Good
Energy Management
Power Flow: Battery → VFD → Motor → Wheels
Regenerative Braking:
· Motor becomes a generator during braking
· Recovers kinetic energy → charges battery
· Extends driving range by 10–25%
EV Powertrain Feedback Loops:
BMS – SOC, voltage, temperature data
Motor Encoder – real-time speed & position
Current & Temp Sensors – phase & thermal monitoring
Thermal Management
Safe: < 85°C · Caution: 85–100°C · Shutdown: > 100°C
Cooling Strategies:
Passive – Heatsinks & natural convection (low power)
Forced Air – Fans for medium-power VFDs
Liquid – Glycol circuits for 300+ kW inverters
Integrated – Motor-frame cooling for optimal path
Advanced Features:
AWD multi-motor coordination; AI predictive energy mgmt;
adaptive torque vectoring; wireless charging integration
Fault Detection & Safety Systems
L1: Over-Current Protection – Instant shutdown if current > limit
L2: Over-Temperature Monitoring – Alert & derate at 85°C, shutdown at 100°C
L3: DC Bus Voltage Monitoring – Range 250–450 V; auto-shutdown if out of range
L4: Sensor Failure Detection – Monitors current, voltage & temperature sensors
L5: Emergency Isolation – Contactor opens, motor disabled immediately
Performance Metrics
System Efficiency: 92–95%
Torque Response: < 10 ms
Speed Control: ± 1% Accuracy
Power Density: 4–8 kW/kg
Range Improvement: 8–15%
Cost per kW: $15–25/kW
(Typical modern EV VFD systems)
Future Trends & Conclusion
SiC Semiconductors – 50% efficiency gains
GaN Devices – Higher switching frequencies
AI-driven Control – Real-time optimization
Wireless Power – Dynamic charging while driving
Integrated Battery-Inverter – Reduced complexity
Conclusion:
VFDs are fundamental to modern EV performance;
advances in semiconductors will drive further gains.
Smart Motor Control in EVs using VFD | Comprehensive Technical Analysis

## Slide 3
Thank You