## Slide 1
VFD & HMI
Logging Function
and Time Action
Nedungkilli I
RA2512053010007

## Slide 2
Introduction
Logging Function
The logging function in VFD and HMI systems records operational data such as speed, current, voltage, and fault events over time. It serves as a critical tool for monitoring drive performance and ensuring system reliability.
Time Action
Time action in VFD and HMI refers to scheduled or timed control sequences that automate drive operations based on predefined time conditions. It enables hands-free control of motors and processes without manual intervention.

## Slide 3
Applications
Logging Function
Time Action
Fault History Logging
Logs VFD fault codes with timestamps, helping technicians diagnose and resolve recurring issues quickly.
Parameter Change Logging
Records any VFD parameter modifications in the HMI, providing a clear audit trail for maintenance and compliance.
Scheduled Start/Stop Control
Automatically starts and stops the VFD-driven motor at fixed times, reducing operator dependency.
Time-Based Speed Adjustment
Adjusts VFD output frequency at different times of the day to match production demand automatically.

## Slide 4
Working Principle
Logging Function
Time Action
1. Data Sampling & Storage
The HMI polls the VFD at regular intervals to read parameters like frequency, current, and voltage, then time-stamps and stores them in log memory for chronological records.
2. Event-Triggered Fault Capture
When the VFD detects a fault (overcurrent, overload, etc.), the HMI instantly logs the fault code, timestamp, and last known operating values for accurate diagnosis.
1. RTC Based Scheduling
The HMI uses its built-in Real-Time Clock (RTC) to match pre-programmed time conditions and automatically sends Run, Stop, or Setpoint commands to the VFD via Modbus or Profibus.
2. Condition-Based Time Logic
The HMI executes time actions only when both a time condition and a process condition are met (e.g., "Start at 08:00 AM only if Tank Level > 50%"), ensuring safe and process-aware control.

## Slide 5
Conclusion
Implement logging and time-action features to enable proactive maintenance and reliable automation.
Ensure clock synchronization, secure log storage, and integration with enterprise monitoring for optimal results.
T H A N K Y O U