## Slide 1: 20MEC521J Fundamentals of Robotic systems Unit I

## Slide 2: Unit I
1 | Introduction to Robotics, History - Developments in Robotics
2 | Robot anatomy, Definition and law of robotics
3 | Terminology of Robotics, Accuracy and repeatability, dexterity, compliance
4 | RCC device of Robotics-Simple problems
5 | Specifications of Robot-Speed of Robot- Robot joints and links
6 | Robot Drive Systems-Hydraulic, Pneumatic and Electric system.
7 | Mechanical grippers-Slider crank mechanism, Screw type
8 | Rotary actuators, cam type-Magnetic grippers- Vacuum grippers
9 | Gripper force analysis, Gripper selection and design

## Slide 3
Definition (RIA – Robot institute of america)
“ A reprogrammable, multifunctional manipulator designed to move material, parts, tools, or specialized devices through various programmed motions for the performance of a variety of tasks”

## Slide 4: Definition – (International Organization for Standardization -ISO):
“An automatically controlled, reprogrammable, multipurpose manipulator programmable in three or more axes, which can be either fixed in place or mobile for use in industrial automation applications”

## Slide 5: To qualify as a robot, a machine must be able to:
1) Sensing and perception: get information from its surroundings
2) Carry out different tasks: Locomotion or manipulation, do something physical–such as move or manipulate objects
3) Re-programmable: can do different things
4) Function autonomously and/or interact with human beings

## Slide 6: Three Laws of Robotics
FIRST LAW: Do not harm human being
A robot must not harm a human being, or, through inaction, allow a human being to come to harm.
SECOND LAW: Obey human being
A robot must always obey the orders given it by human beings except where such orders would conflict with the First Law.
THIRD LAW: Protects itself from harm
A robot must protect its own existence as long as such protection does not conflict with the First or Second Law.

## Slide 7: Components of robotic system
Various Components : 1.Base 2.Links and Joints 3.End-effector / gripper 4.Wrist 5.Drive / Actuator 6.Controller 7.Sensors

## Slide 8: Serial Manipulator

## Slide 9: Parallel Manipulator

## Slide 10: Robot Anatomy
Manipulator consists of joints and links
  Joints provide relative motion
  Links are rigid members between joints
  Various joint types: linear and rotary
  Each joint provides a “degree-of-freedom”
  Most robots possess five or six degrees-of-freedom
Robot manipulator consists of two sections:
  Body-and-arm – for positioning of objects in the robot's work volume
  Wrist assembly – for orientation of objects

## Slide 11: Robot Anatomy

## Slide 12: Degrees of freedom (DOF)
DOF / Connectivity is defined as one of the variable required to define the motion of the body in space.
Degree of freedom of a system depends on the number of variable or coordinates that are needed to describe its position.
Each joint in a robotic system gives the robot one degree of freedom.

## Slide 13: The Robotic Joints
A robot joint is a mechanism that permits relative movement between parts of a robot arm.
The joints of a robot are designed to enable the robot to move its end - effector along a path from one position to another as desired.

## Slide 14: The Robotic Joints
These degrees of freedom, independently or in combination with others, define the complete motion of the end-effector.
These motions are accomplished by movements of individual joints of the robot arm. The joint movements are basically the same as relative motion of adjoining links.
Depending on the nature of this relative motion, the joints are classified as prismatic or revolute.

## Slide 15: The Robotic Joints
Prismatic joints (L) are also known as sliding as well as linear joints.
They are called prismatic because the cross section of the joint is considered as a generalized prism. They permit links to move in a linear relationship.

## Slide 16: The Robotic Joints
Revolute joints permit only angular motion between links. Their variations include:
  Rotational joint (R)
  Twisting joint (T)
  Revolving joint (V)

## Slide 18: Mechanical Joints for Robots
Translational motion - Prismatic joints
  Linear joint (type L)
  Orthogonal joint (type O)
Rotary motion - Revolute joints
  Rotational joint (type R)
  Twisting joint (type T)
  Revolving joint (type V)

## Slide 19: Translational Motion Joints
Linear joint
Type L joint; the relative movement between the input link and the output link is a translational sliding motion, with the axes of the two links parallel.

## Slide 20: Translational Motion Joints
Orthogonal joint
Type O joint; the relative movement between the input link and the output link is a translational sliding motion, but the output link is perpendicular to the input link.

## Slide 21: Rotary motion
Rotational joint
Type R joint; this provides rotational relative motion, with the axis of rotation perpendicular to the axes of the input and output links.

## Slide 22: Rotary motion
Twisting joint
Type T joint; this provides rotary motion, but the axis of rotation is parallel to the axes of the two links.

## Slide 23: Rotary motion
Revolving joint
Type V joint; the axis of the input link is parallel to the axis of rotation of the joint, and the axis of the output link is perpendicular to the axis of rotation.

## Slide 24: Constraints???

## Slide 25: DOF??
1 DOF - Rovolute
1 DOF - Prismatic

## Slide 26
2 DOF – Cylindrical joint
2 DOF – Hooke joint
3 DOF – Ball and Socket joint

## Slide 29: Name the joints? DOF?

## Slide 30: DOF
A point in 2-D:
A point in 3-D space:
A rigid body in 3-D:
Spatial Manipulator:
Planar Manipulator:
2 DOF
3 DOF
6 DOF
6 DOF
3 DOF

## Slide 31
Redundant Manipulator:
Either a Spatial Manipulator with more than 6 dof or a Planar Manipulator with more than 3 dof
Under-actuated Manipulator
Either a Spatial Manipulator with less than 6 dof or a Planar Manipulator with less than 3 dof

## Slide 32: Exercise
Draw the following configurations
  LRL - ORO
  RRL - RRO
  TRL
  LVL - OVO

## Slide 34
Sketch following manipulator configurations
(a) TRT:R, (b) TVR:TR, (c) RR:T.
Solution:

## Slide 35: Joint representations
Symbols of joints (arrows show direction of motion). (a) Prismatic joint. (b) Revolute joint
1. (c) Revolute joint 2. (cl) Up-and-down rotation. (c2) Back-and-forth rotation.

## Slide 36: Can you name the common coordinate systems in robots????
Cartesian coordinate system
Cylindrical coordinate system
Polar or Spherical coordinate system
Revolute coordinate system

## Slide 37: Robot Body-and-Arm Configurations
Five common body-and-arm configurations for industrial robots:
  Polar coordinate body-and-arm assembly
  Cylindrical body-and-arm assembly
  Cartesian coordinate body-and-arm assembly
  Jointed-arm body-and-arm assembly
  Selective Compliance Assembly Robot Arm (SCARA)
Function of body-and-arm assembly is to position an end effector (e.g., gripper, tool) in space

## Slide 38: Work volume (Work envelope)
    Volume in which the robot is able to work.
The work volume is determined by the following physical characteristics of the robot:
  The robots physical configuration
  The size of the body, arm, and wrist components
  The limits of the robots joint movements.
  Dextrous Workspace
  It is the volume of space, which the robot’s end-effector can reach with various orientations
  Reachable Workspace
  It is the volume of space that the end-effector can reach with one orientation

## Slide 39: ROBOT CLASSIFICATION
Cartesian Configuration:
Robots with Cartesian configurations consists of links connected by linear joints (L). Gantry robots are Cartesian robots (LLL).
Also known as rectilinear robot and x-y-z robot. Consists of three sliding joints, two of which orthogonal (O joint).

## Slide 40
Cartesian Coordinate Body-and-Arm Assembly
A robot with 3 prismatic joints – the axes consistent with a Cartesian coordinate system.
Commonly used for:
pick and place work
assembly operations
handling machine tools
arc welding

## Slide 41
Advantages
    Linear motion in three dimension
    Simple kinematic model
    Rigid structure
    Higher repeatability and accuracy
    High lift-carrying capacity as it doesn’t vary at different locations in work volume
    Easily visualize
    Can increase work volume easily
    Inexpensive pneumatic drive can be used for P&P operation
Notes: 41
29 October 2020
Cont.

## Slide 42
Disadvantages
    requires a large volume to operate in
    work space is smaller than robot volume
    unable to reach areas under objects
    must be covered from dust
Applications
    Assembly
    Palletizing and loading-unloading machine tools,
    Handling
    Welding
Notes: 42
29 October 2020
Cont.

## Slide 43: Cartesian Robot - Work Envelope

## Slide 44: Can you draw Orthogonal-coordinate type robot? (Symbolic representation)

## Slide 45: Cylindrical coordinate
Consists of a vertical column, relative to which an arm assembly is moved up or down. The arm can be moved in and out relative to the axis of the column. Common configuration is to use a T joint to rotate the column about its axis. An L joint is used to move the arm assembly vertically along the column, while an O joint is used to achieve radial movement of the arm.

## Slide 46
Advantages
    Simple kinematic model
    Rigid structure & high lift-carrying capacity
    Easily visualize
    Very powerful when hydraulic drives used
Disadvantages
    Restricted work space
    Lower repeatability and accuracy
    Require more sophisticated control
Applications
    Palletizing, Loading and unloading
    Material transfer, foundry and forging

## Slide 47: Cylindrical Robot - Work Envelope

## Slide 48: Can you draw Cylindrical-coordinate type robot? (Symbolic representation)

## Slide 49: Polar Coordinate Body-and-Arm Assembly
Notation TRL:
Consists of a sliding arm (L joint) actuated relative to the body, which can rotate about both a vertical axis (T joint) and horizontal axis (R joint)
Polar robots have a work space of spherical shape. Generally, the arm is connected to the base with a twisting (T) joint and rotatory (R) and linear (L) joints follow.

## Slide 50: Spherical/Polar Robots
A robot with 1 prismatic joint and 2 rotary joints – the axes consistent with a polar coordinate system.
Commonly used for:
handling at die casting or fettling machines
handling machine tools
arc/spot welding

## Slide 51
Advantages
    Covers a large volume
    Can bend down to pick objects up off the floor
    Higher reach ability
Disadvantages
    Complex kinematic model
    Difficult to visualize
Applications
    Palletizing
    Handling of heavy loads e.g. casting, forging

## Slide 52: Spherical Robot - Work Envelope

## Slide 53: Can you draw Polar-coordinate type robot? (Symbolic representation)

## Slide 54: ROBOT CLASSIFICATION
The designation of the arm for this configuration can be TRL or TRR.
Robots with the designation TRL are also called spherical robots. Those with the designation TRR are also called articulated robots. An articulated robot more closely resembles the human arm.

## Slide 55
Articulated Robots
A robot with at least 3 rotary joints.
Commonly used for:
assembly operations
welding
weld sealing
spray painting
handling at die casting or fettling machines

## Slide 56
Advantages:
all rotary joints allows for maximum flexibility
any point in total volume can be reached.
all joints can be sealed from the environment.
Disadvantages:
extremely difficult to visualize, control, and program.
restricted volume coverage.
low accuracy
Articulated Robots

## Slide 57: Joint-arm Configuration
The jointed-arm is a combination of cylindrical and articulated configurations. The arm of the robot is connected to the base with a twisting joint. The links in the arm are connected by rotatory joints. Many commercially available robots have this configuration.
General configuration of a human arm, this consists of a vertical column that swivels about the base using a T joint. At the top of the column is a shoulder joint (an R joint), output to an elbow joint (another R joint).

## Slide 58: Joint-arm Configuration

## Slide 59
Advantages
    Maximum flexibility
    Cover large space relative to work volume objects up off the floor
    Suits electric motors
    Higher reach ability
Disadvantages
    Complex kinematic model
    Difficult to visualize
    Structure not rigid at full reach
Applications
    Spot welding, Arc welding

## Slide 60
Jointed Arm - Work envelope

## Slide 61: Can you draw Jointed Arm type robot? (Symbolic representation)

## Slide 62
Selective Compliance Assembly Robot Arm. Similar in construction to the jointer-arm robot, except that the shoulder and elbow rotational axes are vertical, which means that the arm is very rigid in the vertical direction, but compliant in the horizontal direction.
SCARA Robots
(Selective Compliance Articulated Robot Arm)

## Slide 63
A robot with at least 2 parallel rotary joints.
Commonly used for:
pick and place work
assembly operations
SCARA Robots
(Selective Compliance Articulated Robot Arm)

## Slide 64
Can you draw SCARA type robot? (Symbolic representation)

## Slide 65
Configuration | Advantages | Disadvantages
Cartesian coordinates | 3 linear axes, easy to visualize, rigid structure, easy to program | Can only reach front of itself, requires large floor space, axes hard to seal
Cylindrical coordinates | 2 linear axes +1 rotating, can reach all around itself, reach and height axes rigid, rotational axis easy to seal | Can’t reach above itself, base rotation axis as less rigid, linear axes is hard to seal, won’t reach around obstacles
SCARA coordinates | 1 linear + 2 rotating axes, height axis is rigid, large work area for floor space | 2 ways to reach point, difficult to program off-line, highly complex arm
Spherical coordinates | 1 linear + 2 rotating axes, long horizontal reach | Can’t reach around obstacles, short vertical reach
Revolute coordinates | 3 rotating axes can reach above or below obstacles, largest work area for least floor space | Difficult to program off-line, 2 or 4 ways to reach a point, most complex manipulator

## Slide 67: Working Envelope

## Slide 69: Wrist Configurations
Wrist assembly is attached to end-of-arm
End effector is attached to wrist assembly
Function of wrist assembly is to orient end effector
  Body-and-arm determines global position of end effector
Two or three degrees of freedom:
  Roll
  Pitch
  Yaw

## Slide 70: Six basic robot motions are ???
Radial traverse: Involve the extension and retraction (in or out movement) of the arm relative to the base
Vertical traverse: Provide up-and-down motion of the arm
Rotational traverse: Rotation of the arm about vertical axis such as left-and-right swivel of the robot arm about a base
Wrist Pitch/Bend: Provide up-and-down rotation to the wrist
Wrist Yaw: Involve right-and-left rotation of the wrist
Wrist Roll/Swivel: Is the rotation of the wrist about the arm axis

## Slide 72: Spatial Resolution
Notes: 72
29 October 2020
Cont.

## Slide 73: Spatial Resolution
Defined as smallest increment of movement into which the robot can divide its work volume
Depends on two factors: system’s control resolution and the robot’s mechanical inaccuracies
Control resolution is determined by robot’s position control system and its feedback measurement system
Ability to divide total range of movement for the particular joint into individual increments that can be addressed in the controller
The increments are sometimes referred to as “ addressable points”
Notes: 73
29 October 2020
Cont.

## Slide 74
Joint range depends on the bit storage capacity in the control memory
Number of increments for a axis is given by
Number of Increments = 2n
n = the number of bits in the control memory
Have a control resolution for each joint in case of several DOF
Total control resolution depend on the wrist motions as well as the body and arm motions
Spatial Resolution
Notes: 74
29 October 2020
Cont.

## Slide 75
Mechanical inaccuracies come from elastic deflection in the structure elements, gear backlash, stretching of pulley cords, leakage of hydraulic fluids and other imperfections in the mechanical system
Also affected by load being handled, the speed of arm moving, condition of maintenance of robot
Spatial Resolution
Notes: 75
29 October 2020
Cont.

## Slide 76: Accuracy
Ability to position its wrist end at a desired target point within the work volume
Depends on spatial resolution means how closely the robot can define the control increments
One half of the control resolution by ignoring the mechanical inaccuracies
Notes: 76
29 October 2020
Cont.

## Slide 77
Notes: 77
29 October 2020
Cont.

## Slide 78: Repeatability
Ability to position its wrist at a point in space that had been taught
Accuracy relates to its capacity to be programmed to achieve a given target point
Programmed point and target point may be different due to limitations of resolution
Repeatability refers to ability to return to the programmed point when commanded to do so
Notes: 78
29 October 2020
Cont.

## Slide 80: Robot drive systems

## Slide 81: Drive Systems
Capacity to move robot’s body, arm and wrist
Determine speed of the arm movements, strength of the robot & dynamic performance
Type of applications that the robot can accomplish
Powered by three types of drive systems:
      Hydraulic
      Pneumatic
      Electric
Notes: 81
29 October 2020
Cont.

## Slide 82
Notes: 82
29 October 2020
Cont.

## Slide 83
Hydraulic Drive
Linear piston or rotary vane types.
High power-to-weight ratio suitable for high loads at moderate speeds.
Easily controllable due to high stiffness of hydraulic system.
Require high energy storage systems such as pumps and accumulators.
Susceptible to leakage, which may reduce efficiency.
Require filtration.
Air entrapment and cavitation may cause difficulties.
Servo valves controlling the fluid flow must be placed close to the actuators to increase the stiffness of the control system.
Suitable for harsh environments caused by dust, dirt, and moisture.

## Slide 84
Hydraulic Drive
  Associated with large robot
  Provide greater speed & strength
  Add floor space
  Leakage of oil
  Provide either rotational or linear motions
  Applications such as:
      Spray coating robot
      Heavy part loading robot
      Material handling robot
      Translatory motions in cartesian robot
      Gripper mechanism
Notes: 84
29 October 2020
Cont.

## Slide 85
Hydraulic Drive..
Notes: 85
29 October 2020
Cont.

## Slide 86
Used in inexpensive manipulators with low load-carrying capacity.
Usually require mechanical stops for accurate positioning in non-servo control.
Single- and double-acting piston or rotary vane types are commonly used.
Inherently lightweight at moderate operating pressures.
Limited by low efficiency at reduced loads and low stiffness due to compressibility.
Pneumatic actuators

## Slide 87
Pneumatic Drive
  Reserved for smaller robot
  Limited to “pick-and-place” operations with fast cycles
  Drift under load as air is compressible
  Provide either rotational or linear motions
  Simple and low cost components
  Used to open and close gripper
Notes: 87
29 October 2020
Cont.

## Slide 88
Provide a variety of power systems.
Easier to control.
May not be as responsive as hydraulic systems and stiffer than pneumatic systems with low pressure.
Normally require speed reducers, which introduce inefficiency and error in operation.
Variety of types such as permanent magnet DC motors, printedcircuit motors , stepping motors, and direct drives.
Electric motors

## Slide 89
Electric Drive
  Rotor, stator, brush and commutator assembly
  Rotor has got windings of armature and stator has got magnets
  The brush and the commutator assembly switch the current in armature windings
  The most commonly used are DC servomotors, AC servomotors and stepper motors
Notes: 89
29 October 2020
Cont.

## Slide 90
Robot Controls with Hydraulic, Pneumatic, and Electric Systems

## Slide 91: Speed of motion and Load carrying capacity
Speed depends on the following factors
The accuracy with which the end effector must be positioned
The weight of the object being manipulated
The distance to be moved

## Slide 92: Speed of motion and Load carrying capacity
Can you tell me how much load you can carry??
The load carrying capacity should be specified under the condition that the robots arm is in its weakest position.

## Slide 93: End effectors

## Slide 94: Classification
Two categories of end effectors are
    Grippers
    Tools
According to the types of grasping, the end effectors are grouped in to
    Mechanical fingers
    Special tools
    Universal fingers

## Slide 95
Tools are used in applications where the robot must perform some processing operation on the part. Examples of the tools are:
    Spot welding gun.
    Arc welding tool.
    Spray painting gun.
    Rotating spindle for drilling, grinding, and so forth.
    Assembly tool (e.g. automatic screw driver)
    Heating torch.

## Slide 96: Types of grippers
Mechanical grippers
Hooking or lifting grippers
Grippers for scooping or ladling powders or molten metals or plastics
Vacuum cups (Negative Pressure)
Magnetic grippers
Adhesive
Electrostatic grippers

## Slide 97: Mechanical grippers
It uses mechanical fingers actuated by a mechanism to grip an object.
Various mechanisms used in mechanical grippers are
  Linkage
  Gear and rack
  Cam
  Screw
  Cable and pulley, etc.,
  The grippers can actuate the opening or closing of the fingers by
  Pivoting or swinging movement
  Linear or translational movement

## Slide 98: Mechanical grippers
The function of the gripper mechanism is to translate some form of power input into the grasping action of the fingers against the part.
There are two ways of constraining the part in the gripper.
By physical constriction of the part within the fingers – this is usually accomplished by the contacting surfaces of the fingers to ne in the approximate shape of the work geometry
By friction between the fingers and the workpart – the fingers must apply a force that is sufficient for friction to retain the part against gravity, acceleration, and any other force that might arise during the holding portion of the work cycle.

## Slide 99
By physical constriction of the part within the fingers
By friction between the fingers and the workpart

## Slide 100
The part might slip out of the gripper if the applied force is insufficient.
To resist this slippage, the gripper must be designed to exert a force that depends on the weight of the object, the co-efficient of friction between the part surface and the finger, the acceleration of the part and the orientation between the direction of motion during acceleration and the direction of fingers.

## Slide 101: Types of mechanical actuation - Pivoting or swinging movement
Linkage actuation:

## Slide 102
Rack and Pinion actuation:
A rack actuated by a hydraulic / pneumatic cylinder operates two pivoted pinions.
The fingers attached to the racks open and close to grab and release the object.

## Slide 103
CAM actuation:
A cam attached to a cylinder moves to and fro.
Spring loaded followers moves on the cam profile.
The finger pads attached to the pivoted liver connected to the followers open and close to release and grab the object

## Slide 104
Screw actuation:
A threaded block engages with a screw moves forward and backward, the fingers attached to levers connected to the threaded block by a hinged joint, open and close providing releasing and gripping action.
The screw is rotated by a motor through reduction box.

## Slide 105: Types of mechanical actuation –translational movement

## Slide 106: Gear and Rack Grippers
movement of input due to gear motion which makes connecting links to go in motion to make gripping action at the output link.
http://sra.vjti.info/knowledgebase/posts-on-a-roll-1/gripper-mechanisms

## Slide 107: Three Fingered Grippers
http://sra.vjti.info/knowledgebase/posts-on-a-roll-1/gripper-mechanisms

## Slide 108: Vacuum Grippers link
for non-ferrous components with flat and smooth surfaces, grippers can be built using standard vacuum cups or pads made of rubber-like materials. Not suitable for components with curved surfaces or with holes.
http://sra.vjti.info/knowledgebase/posts-on-a-roll-1/gripper-mechanisms

## Slide 109: Magnetic Gripper
http://sra.vjti.info/knowledgebase/posts-on-a-roll-1/gripper-mechanisms
gripper

## Slide 110: GRIPPER FORCE ANALYSIS
The fig. shows the linkage mechanism and dimensions of a gripper used to handle a workpart for a machining operation. Suppose it has been determine that the gripper force is to be 25 N. What is required is to compute the actuating force to deliver this force of 25 N.

## Slide 111
Due to symmetry of the gripper consider only one half of the mechanism.
Moments :-
25(4cos 15°) = Fsin 45°(1.5cos15°) + Fcos45°(1.5sin15°)
96.6 = F(1.0246+0.2745) =1.2991F
F = 74.4 N
The actuation force applied to the plunger to deliver this force of 74.4 N to each finger.
So,
Fa = 2 X 74.4 X cos45°
Fa = 105.2 N

## Slide 112: GRIPPER FORCE ANALYSIS

## Slide 118
A Cartesian robot has a horizontal reach of 450 mm and a horizontal stroke of 250 mm. What is the maximum limit within which the object placed is not reachable?

## Slide 121: CONSIDERATIONS IN GRIPPER SELECTION AND DESIGN
The important factors that determine the required grasping force are:
The weight of the object. Consideration of whether the part can be grasped consistently about its center of mass. If not, an analysis of the possible moments from off-center grasping should be considered.
The speed and acceleration with which the robot arm moves (acceleration and deceleration forces), and the orientational relationship between the direction of movement and the position of the fingers on the object (whether the movement is parallel or perpendicular to the finger surface contacting the part)
Whether physical constriction or friction is used to hold the part.
Coefficient of friction between the object and the gripping fingers.

## Slide 123: Gripper design considerations

## Slide 124: Gripper design considerations

## Slide 125: Selection consideration of gripper

## Slide 126: Checklist of factors in the selection and design of grippers
Factor | Consideration
Part to be handled | Weight and size Shape Changes in shape during processing Tolerances on the part size Surface condition, protection of delicate surfaces
Actuation method | Mechanical grasping Vacuum cup Magnet Other methods (adhesives, scoops, etc.)

## Slide 127: Checklist of factors in the selection and design of grippers
Factor | Consideration
Power and signal transmission | Pneumatic Electrical Hydraulic Mechanical
Gripper force (mechanical gripper) | Weight of the object Method of holding (physical constriction or friction) Coefficent of firction between fingers and object Speed and acceleration during motion cycle
Positioning problems | Length of finger's Inherent accuracy and repeatability of robot Tolerances on the part size

## Slide 128
Factor | Consideration
Service conditions | Number of actuations during lifetime of gripper Replaceabilty of wear components (fingers) Maintenance and serviceability
Operating environment | Heat and temperature Humidity, moisture, dirt, chemicals
Temperature protection | Heat shields Long fingers Forced cooling (compressed air, water cooling, etc.) Use of heat-resistant materials
Checklist of factors in the selection and design of grippers

## Slide 129
Factor | Consideration
Fabrication materials | Strength, rigidity, durability Fatigue strength Cost and ease of fabrication Friction properties for finger surfaces Compatibility with operating environment
Other considerations | Use of interchangeable fingers Design standards Mounting connections and interfacing with robot Risk of product design changes and their effect on the gripper design Lead time for design and fabrication Spare parts. maintenance, and service
Checklist of factors in the selection and design of grippers

## Slide 130: General architecture of a robotic mechanical system

## Slide 131: CLASSIFICATION OF ROBOTICS
■ Robotic Manipulator
■ Wheeled Mobile Robots (WMR)
■ Legged Robots
■ Underwater Robots and Flying Robots
■ Robot Vision
■ Artificial Intelligence
■ Industrial Automation

## Slide 132: Industrial Robot Applications