## Slide 1
REAL TIME EMBEDDED SYSTEMS (21EIC504J)
ARM ASSEMBLY PROGRAMMING
Module-2 Seminar: Architecture & Instructions
Presented by: Mohamed Sabiq
MTech • Automation & Robotics

## Slide 2
Seminar Agenda
Instruction Set Basics
Register Map (Cortex-M)
Load-Store Architecture
Data Processing Ops
Control Flow & Loops
Barrier & Saturation
This flow matches the Module-2 syllabus topics, focusing on technical depth for postgraduate study.

## Slide 3
Command Language
The ISA is the CPU's native interface. Every command is defined by an Opcode and associated Operands.
RISC Principles
ARM uses Reduced Instruction Set Computing (RISC). It prioritizes register-to-register operations for predictable execution.
• Fixed-length instructions • Single-cycle execution (mostly) • Load-Store Model
What is an Instruction Set?
Assembly is basically the CPU’s direct language. Each instruction translates directly to a machine code bit pattern.

## Slide 4
R0 – R12: General Purpose Registers for data processing.
R13 (SP): Stack Pointer. Points to the current stack top.
R14 (LR): Link Register. Stores return address for functions.
R15 (PC): Program Counter. Points to next instruction.
xPSR: Status flags (Z, N, C, V).
ARM Cortex-M Register Map
NOTE: Most ARM instructions operate directly on registers. R13, R14, and R15 have special hardware functions.

## Slide 5
Load-Store Architecture
In ARM, memory is isolated from the ALU. You cannot perform arithmetic directly on RAM values.
This decoupling allows for higher clock speeds and deterministic timing in RTOS.
This is a very important ARM feature. The processor only manipulates data inside registers.

## Slide 6
LDR / STR Ops
Basic memory access instructions.
Supports offset, pre-index, and post-index addressing modes.
Stack Management
Uses R13 (SP) to manage function context and local variables.
Note: Popping LR into PC performs an automatic function return.
Memory Access & Stack
Stack operations are critical in functions and interrupts to preserve the state of general-purpose registers.

## Slide 7
Example: SUBS R0, R0, #1 (Decrement and update status flags)
ADD / SUB
Standard math operations.
MUL / MLA
Multiply and Multiply-Accumulate.
ADC / SBC
Add/Sub with Carry (for 64-bit ops).
Arithmetic Processing
Arithmetic instructions often update flags (using the 'S' suffix), which helps in making decisions.

## Slide 8
Bitwise Ops: AND, ORR, EOR (XOR), BIC (Bit Clear).
Barrel Shifter: Unique ARM feature to shift an operand during an ALU operation.
Logical Ops & Shifting
Bit operations are used heavily for peripheral registers. The barrel shifter provides 'free' scaling in many instructions.

## Slide 9
ZNCV
STATUS FLAGS
Status Flags (xPSR)
Z (Zero): Result was zero (Equal). N (Negative): Result bit 31 is set. C (Carry): Unsigned overflow. V (Overflow): Signed overflow.
CMP R0, #10 calculates (R0 - 10) and updates flags without saving the result.
Condition Flags & CMP
CMP prepares the CPU for conditional branching by updating the status register flags.

## Slide 10
B: Unconditional Branch.
BEQ / BNE: Branch if Equal / Not Equal.
BL: Branch with Link (Function call).
Control Flow & Branching
This is how loops are built in assembly. SUBS updates flags, and BNE checks the Zero flag.

## Slide 11
Crucial for DMA, Interrupts, and Multicore synchronization.
DMB
Data Memory Barrier. Ensures all memory access finishes before next memory operation.
DSB
Data Sync Barrier. Halts execution until memory access is complete.
ISB
Instruction Sync Barrier. Flushes pipeline and fetches new instructions.
Memory Barrier Instructions
Even if code is correct, hardware can reorder operations—barriers prevent race conditions in real-time peripherals.

## Slide 12
Safe Clamping
Normal overflow "wraps around" (e.g., 127 + 1 = -128). Saturation clamps the result at the maximum or minimum limit.
Essential for: • DSP: Audio/Video filtering • Control: Motor torque limits • Sensors: Noise clamping
Arithmetic Saturation
Saturation avoids dangerous 'wrap-around' values which can cause control instability in real-time systems.

## Slide 13
Summary & Questions
We have explored the ARMv7-M Instruction Set, from fundamental Load-Store models to advanced Safety Barriers and DSP Saturation.
• Register Bank R0-R15 • LDR/STR & Stack Usage • Barrel Shifter Optimization
• Condition Flags & Branches • Pipeline Synchronization • Saturation Safety
Finish with 2–3 questions to make it interactive. Thank you for your time.