## Slide 1
PROJECT PRESENTATION
Autonomous Mobile
Navigation Bot
using LiDAR Mapping
Sabiq RA2512053010005
Chandru RA2512053010012
Nedungkilli RA2512053010007
Vignesh RA2512053010010

## Slide 2
Introduction
Autonomous mobile robots navigate without human intervention, using sensors and algorithms to perceive their surroundings.
A major challenge is operating in unknown environments without prior maps.
Simultaneous Localization and Mapping (SLAM) enables real-time map building while tracking position.
LiDAR and ultrasonic sensors play a key role in environment sensing and obstacle detection.
This project implements SLAM using ROS, optimizing sensor usage for efficient autonomous navigation.

## Slide 3
Abstract
This project develops an autonomous mobile robot capable of navigating its environment without human control. The core goal is achieving Simultaneous Localization and Mapping (SLAM) using ROS — enabling the robot to build a map and track its position simultaneously.
A YDLIDAR X2 sensor provides 360° scanning, while ultrasonic sensors handle short-distance obstacle detection. Due to the Raspberry Pi's limited processing power, a laptop serves as the main computation unit via wireless communication.
An important focus is sensor optimization — varying sensor placement and count to study effective collision avoidance with minimal hardware.

## Slide 4
Objectives
01
SLAM Implementation
Develop an autonomous mobile robot capable of performing Simultaneous Localization and Mapping (SLAM) using ROS for real-time mapping and navigation.
02
Sensor Optimization
Analyze different sensor placements and reduce the number of sensors while maintaining effective collision avoidance performance.

## Slide 5
Components Used
Raspberry Pi 3 Model B
Onboard controller
YDLIDAR X2 2D LiDAR
360° environment scanning
Ultrasonic Sensors HC-SR04
2 units – short-range detection
Motor Driver (L298N)
Wheel drive control
4-Wheel Robotic Chassis
With DC motors
Li-ion Battery Pack
Power supply unit
Laptop
ROS master & SLAM processing

## Slide 6
Methodology
1
Assemble hardware
2
Interface sensors with Raspberry Pi
3
Connect Pi & laptop via WiFi
4
Install & configure ROS
5
Acquire LiDAR & ultrasonic data
6
Implement SLAM
7
Generate map & localize
8
Obstacle avoidance & experiments

## Slide 7
Sensor Optimization
Key Concept
Number Variation
Systematically vary the count of ultrasonic sensors to find the minimum required for reliable collision detection.
Placement Analysis
Test different sensor positions to determine optimal mounting configurations for full coverage and safety.
Trade-off Evaluation
Balance cost, power consumption, processing load, and safety margins across configurations.
Performance Threshold
Identify the minimal sensor set that meets collision-rate thresholds while preserving navigation performance.

## Slide 8
System Overview
Hardware Layer
▸ 4-Wheel chassis with DC motors + L298N motor driver
▸ Raspberry Pi 3 Model B — onboard controller
▸ YDLIDAR X2 — 360° environment scanning
▸ Ultrasonic sensors — short-range obstacle detection
►
Computation & Flow
▸ Laptop runs ROS master + SLAM computation
▸ WiFi bridge: Pi node → Laptop ROS master
▸ Path planning → actuator commands sent back
▸ GPU-accelerated processing where available
Sensors → Pi → WiFi → Laptop ROS → Path Planning → Motors

## Slide 9
Progress Status
✓
Buying
Components
✓
Assembly
●
Working on ROS and programming
CURRENT
4
Final
Product
Step 1
Step 2
Step 3
Step 4

## Slide 10
Current Progress
Progress Details
✓ Completed
✓ Hardware chassis fully assembled and calibration completed
✓ Raspberry Pi configured
✓ Motor driver interfaced
✓ Ultrasonic sensors tested
✓ ROS installed and configured on laptop
✓ Successful communication established between Raspberry Pi and laptop
⏳ Pending
Working on ROS and Programming

## Slide 11
Robot Gallery
📷
[ Insert Photo ]
Original View
📷
[ Insert Photo ]
Top View
📷
[ Insert Photo ]
Front View

## Slide 12
Contributors
Sabiq
RA2512053010005
Programming & ROS
Raspberry Pi programming and ROS configuration
Chandru
RA2512053010012
Hardware Assembly
Assembly of the robot project
Nedungkilli
RA2512053010007
Component Acquisition
Component sourcing and presentation support
Vignesh
RA2512053010010
Documentation
Presentation design and final report

## Slide 13
Expected Results & Conclusions
🗺
Successful SLAM implementation for real-time mapping and localization
🛡
Effective obstacle detection and collision avoidance using LiDAR and ultrasonic sensors
📡
Reliable wireless communication between Raspberry Pi and laptop via ROS
⚡
Optimized sensor placement — reduced hardware with maintained navigation performance
💡
Demonstrates a cost-effective, efficient approach to autonomous mobile robotics

## Slide 14
THANK YOU
Autonomous Mobile Navigation Bot using LiDAR Mapping
SLAM · ROS · LiDAR · Raspberry Pi